## Slide 1: SINSIN A Radio Localization Method August 2023
This project has received funding from the European Union’s Horizon 2020 research innovation programme, administered by EUSPA under grant No. 776253
Agenda
The Technology
Operational Benefits
Present Implementation

## Slide 2
SINSIN Scope
SINSIN is a technology for independent (of GNSS) localization of remote radio beacons
Enhancing C/S MEOSAR
Enabling line of sight localization without satellites
Supporting FGB/ SGB; agnostic to transmission frequency, modulation
Implemented in s/w at the beacon and receiver
Compatible with C/S standards
SINSIN inside
SINSIN inside
SINSIN inside
406MHz
L-band
S-band

## Slide 3
SINSIN Operation Principle
The beacon sets TOE such that the receiver could guess,
enabling TOA based localization with less satellites in view, even directly
Navigation (GNSS) equations
C*(TOAi–TOE) = √[(x-xi)2 + (y-yi)2 + (z-zi)2] unknown: receiver (x, y, z), rx clock drift
Localization (C/S) equations
C*(TOAi–TOE) = √[(x-xi)2 + (y-yi)2 + (z-zi)2]
unknown: beacon (x, y, z), TOE
(x, y. z)
SINSIN

## Slide 4
SINSIN Operational Benefits (1)
Geographical coverage
3 satellites
coverage
4 satellites
coverage
Calculated and Illustrated by Thales Alenia Space

## Slide 5
SINSIN Operational Benefits (2)
Accuracy
SGB | 10 min, 95% |  | 20 min, 95% |  | 30 min, 95% | 
 | standard | SINSIN | standard | SINSIN | standard | SINSIN
3 sats | 1500m | 980m | 1390m | 630m | 1250m | 560m
4 sats | 520m | 430m | 430m | 300m | 280m | 150m
/ Search Time
Calculated by Thales Alenia Space

## Slide 6
SINSIN Operational Benefits (3)
Availability
Tested and Reported by C/S Secretariat

## Slide 7
SINSIN Operational Benefits (4)
Direct line-of-sight localization
406MHz receiver
SINSIN inside
406MHz
Radio beacon
SINSIN inside

## Slide 8
SINSIN Implementation in MEOSAR
SINSIN inside
x2 accuracy
on average

## Slide 9
SINSIN Verification
Demonstrated at C/S conference in Qatar, 2019
  Beacon in Doha, MEOLUT in Toulouse
  Relayed by Galileo satellites
2 sats standard
3 sats standard
2 sats SINSIN
3 sats SINSIN
Real Location
< 5,000Km <
reporting
FGB

## Slide 10
SINSIN Enabled Modules
SINSIN FGB (type approved)
SINSIN SGB chip
SINSIN MEOLUT
406 MHz receiver

## Slide 11
Thank you for your attention !
Daniel Katz
Mobit Telecom
www.sat406.com